## Slide 1
Introduction
1-1
MITM 306: Advanced Computer Networks & Internetworking
4 Credits (2 credits theory + 2 credits lab)
Course Instructors:
Prof. Dr. Md. Shariful Islam
shariful@iit.du.ac.bd, shariful.islam@gmail.com
Notes: 1
1

## Slide 2
Introduction
1-2
MITM 306: Advanced Computer Networks & Internetworking
Book: Computer Networking – A Top Down Approach – Featuring the Internet by J. Kurose and K. Ross (6E)
Reference books:
IEEE 802 Wireless Systems
Data Communications and networking by Forouzan
Resources from Internet
Syllabus:
Chapter 1 – Introduction to computer networks and the Internet
Chapter 2 – Application layer: HTTP, SMTP, DNS etc.
Chapter 3 -Transport Layer Protocols, Congestion Control
Chapter 4 – Network Layer
Chapter 5 -Data Link Layer, WLAN and IEEE 802.11 Medium Access Control
Notes: 2
2

## Slide 3
Introduction
1-3
Course Administration
Mid-term exams ( 25 marks):
Prescheduled MT# 1 – 25 marks
Assignments (15 Marks):
At least 4 assignments will be given
Mostly problem solving from the exercises
Class Attendance (10 Marks):
Final Examination (50 Marks):
Lab : (50 Marks):
Notes: 3
3

## Slide 4
Introduction
1-4
Chapter 1 Introduction
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: 5

## Slide 5
Introduction
Chapter 1: introduction
our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example
overview:
what’s the Internet?
what’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history
1-5
Notes: 6
6

## Slide 6
Introduction
Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
1-6
Notes: 7
7

## Slide 7
Introduction
What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
1-7
Notes: 8
8

## Slide 8
Introduction
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What’s the Internet: “nuts and bolts” view
mobile network
global ISP
regional ISP
home
network
institutional
network
1-8
Notes: 9
9

## Slide 9
Introduction
What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
1-9
Notes: 10
10

## Slide 10
Introduction
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?
1-10
Notes: 11
11

## Slide 11
Introduction
Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
1-11
Notes: 12
12

## Slide 12
Introduction
A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network
1-12
Notes: 13
13

## Slide 13
Introduction
Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
1-13
Notes: 14
14

## Slide 14
Introduction
Enterprise access networks (Ethernet)
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)
1-14
Notes: 15

## Slide 15
Introduction
Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft)
  802.11b/g (WiFi): 11, 54 Mbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G
to Internet
to Internet
1-15
Notes: 16
16

## Slide 16
Introduction
Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
1-16
Notes: 21
21

## Slide 17
Introduction
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
The network core
1-17
Notes: 22
22

## Slide 18
Introduction
Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
1-18
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)
Notes: 23
23

## Slide 19
Introduction
Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
1-19
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
Notes: 24
24

## Slide 20
Introduction
Alternative core: circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks
1-20
Notes: 26
26

## Slide 21
Introduction
Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
1-21
Notes: 27
27
Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 22
Introduction
Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
1-22
* Check out the online interactive exercises for more examples
Notes: 28
28

## Slide 23
Introduction
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching
1-23
Notes: 29
29

## Slide 24
Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure
Notes: 30
30

## Slide 25
Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Notes: 31
31

## Slide 26
Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Notes: 32
32

## Slide 27
Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Notes: 33
33

## Slide 28
Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Notes: 34
34

## Slide 29
Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Notes: 35
35

## Slide 30
Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Notes: 36
36

## Slide 31
Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Notes: 37
37

## Slide 32
Introduction
Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
1-32
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Notes: 38
38

## Slide 33
Introduction
Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
1-33
Notes: 39
39

## Slide 34
Introduction
How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
1-34
Notes: 40
40

## Slide 35
Introduction
Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop
1-35
Notes: 41
41

## Slide 36
Introduction
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
1-36
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay
Notes: 42
42

## Slide 37
Introduction
Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km
1-37
Notes: 43
43

## Slide 38
Introduction
Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, 1st car arrives at second booth; three cars still at 1st booth.
toll
booth
toll
booth
ten-car
caravan
100 km
100 km
1-38
Notes: 44
44

## Slide 39
Introduction
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
Queueing delay (revisited)
La/R -> 1
1-39
* Check out the Java applet for an interactive animation on queuing and loss
Notes: 45
45

## Slide 40
Introduction
“Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes
1-40
Notes: 46
46

## Slide 41
Introduction
“Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
1-41
* Do some traceroutes from exotic countries at www.traceroute.org
Notes: 47
47

## Slide 42
Introduction
Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
1-42
* Check out the Java applet for an interactive animation on queuing and loss
Notes: 48
48

## Slide 43
Introduction
Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
1-43
Notes: 49

## Slide 44
Introduction
Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
1-44
Notes: 50

## Slide 45
Introduction
Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
1-45
Notes: 51

## Slide 46
Introduction
Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
1-46
Notes: 52
52

## Slide 47
Introduction
Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
1-47
Notes: 53
53

## Slide 48
Introduction
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
Encapsulation
message
M
Ht
M
Hn
frame
1-48
Notes: 54
54

## Slide 49
Introduction
Introduction: summary
covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
you now have:
context, overview, “feel” of networking
more depth, detail to follow!
1-49
Notes: 56
56